Why Device Trees
Are not Static
Heinrich Schuchardt, 2020-05-16
CC-BY-SA-4.0

---
Systems Are Modular
- Baseboard + SoC module
- Hats (Raspberry),
  Capes (BeagleBoard)
- Memory modules

---
Devices Are Hot Pluggable
Even CPUs and Memory can be removed and added at runtime
Linux: Documentation/core-api/memory-hotplug.rst
Linux: Documentation/core-api/cpu_hotplug.rst

---
Is There A Master Device?
- With protocols like CCIX there can be multiple bus masters.
- So in future modular systems it is hard to say whose requirements dictate the “one” device tree.
- Do we need separate device trees per bus master?

---
Configurable IO Routing
- SoCs may have more supported IOs than connected pins.
- The routing of GPIOs is configurable, e.g.
  Raspberry GPIO 18 may be connected to input register, output register, PWM, SPI, PCM Audio.
- PCI-e bifurcation is used to connect multiple devices to one PCI-e connector.

---
Device Configurability
- Many devices contain their own firmware or even FPGA.
- Device firmware changes may make the device appear completely different to the outside world.
- How about
  - Changing functions according to license status
  - Changing CPU ISA via microcode

---
Hardware or Software?
1. vdd_soc: sd0 {
2. regulator-name = "VDD_SOC";
3. regulator-min-microvolt = <1000000>;
4. regulator-max-microvolt = <1170000>;
5. regulator-enable-ramp-delay = <146>;
6. regulator-disable-ramp-delay = <4080>;
7. regulator-ramp-delay = <27500>;
8. regulator-ramp-delay-scale = <300>;
9. regulator-always-on;
10. regulator-boot-on;
11. maxim,active-fps-source = <MAX77620_FPS_SRC_1>;
12. maxim,active-fps-power-up-slot = <1>;
13. maxim,active-fps-power-down-slot = <6>;
14. };

---
DT Nodes as Communication Area
- Necessary properties, e.g.
  - cpu-release-addr in CPU node for CPUs with spin-table enable-method
  - Available memory
- Optional properties, e.g.
  - GRUB passing ‘bootargs’, ‘linux,initrd-start’, ‘linux,initrd-end’ to Linux

---
DT in the Software Stack
- Some devices should only be available in secure world
  - SPI flash for UEFI variables

---
Conclusion
- Device trees are a mishmash of
  - Hardware description
  - Hardware configuration
  - Software configuration
  - Communication area

---
Areas for Improvement
- Separation between hardware and software properties
- Support for hardware modularity
- Software layer specific device trees
- Multiple masters (CPUs, Accelarators)
- Ownership

---
Could Device Trees Be Modular?
Module
Configuration
Interface
Routing
Interface
Module
Configuration